## Slide 2: Life-cycle assessment (LCA)
An attempt to evaluate the environmental impacts of a product or service for the whole life of the product or service – ’from the cradle to the grave’
OR:
An attempt to evaluate the environmental impacts of a product or service on the basis of all the natural resource inputs and emissions to the environment arising from the complete supply chain for that product or service.

## Slide 3: Key questions in LCA
1. What is your product/service (in quantitative terms!) (called functional unit)
2. What emissions to and resource demand from the environment is necessary for the identified product/service? (called Life-Cycle Inventory)
3. How do these processes affect the environment? (called Life-Cycle Impact Assessment)

## Slide 4
1. Functional Unit
Quantified measure of the function of the product or service
Used as a reference for all alternatives
Must be the same for LCA-based comparisons
Drinks packaging
”Packing for 100 litres of water such that it can be stored hygienically and safely and be transported and sold to the consumer”
(NOT: 50 cl Glass bottle vs. 33 cl aluminium can)
Vehicle fuel
”Fuel to drive 100 km with a Volvo V50”
(NOT: 1 litre ethanol vs. 1 litre petrol)
Buildings
”1 m2 heated floor area for 50 years” or ”Residence for 12 people for 50 years”
Notes: Fråga!
Låt dem diskutera, sedan svara.

## Slide 5: 2. Life-cycle Inventory
Break this down into two simpler questions:
What are the processes involved in the production of your product/service?
What are the emissions/resource demands for each of the processes?

## Slide 6: Question 2a. What processes?
Watch this film:
https://www.youtube.com/watch?v=eg-E1FtjaxY
Note down: as many separate non-transport processes as you can that are involved in the production of the spoon

## Slide 7
Oil search
T
Extract- ion
T
Refin- ery
T
Pellet factory
T
Mould-ing
T
Shop
T
Party!
End of life
T
Transport

## Slide 8
Oil search
T
Extract- ion
T
Refin- ery
T
Pellet factory
T
Mould-ing
T
Shop
T
Party!
Resources: Oil, minerals, metal ores, wood, cement, sand, gravel, water …..
Emissions: CO2, CH4, SOx, NOx, Hydrocarbons, nitrates, phosphates heavy metals, organic toxins, dioxins
End of life

## Slide 9: Question 3: Life-cycle Impact Assessment
Results of the Inventory:
We know what is taken (resources) from the environment
We know what is put into the environment (emissions)
Life-cycle impact assessment asks what effect the ’takes’ and the ’puts’ actually has on the environment

## Slide 10
Oil search
T
Extract- ion
T
Refin- ery
T
Pellet factory
T
Mould-ing
T
Shop
T
Party!
Resources: Oil, minerals, metal ores, wood, cement, sand, gravel, water …..
Emissions: CO2, CH4, SOx, NOx, Hydrocarbons, nitrates, phosphates heavy metals, organic toxins, dioxins
End of life
Impacts in the environment
Characterization
Classification
LCIA

## Slide 11
Resources: Oil, minerals, metal ores, wood, cement, sand, gravel, water …..
Emissions: CO2, CH4, SOx, NOx, Hydrocarbons, nitrates, phosphates heavy metals, organic toxins, dioxins
Impacts in the environment
LCIA
Characterization
Classification

## Slide 13: ReCiPe, Goedkoop et al, 2009
1. Classification
2. Characterisation
Notes: End point structure similar to Eco-indicator 99

## Slide 14: Typical Impacts
Typical impacts considered include:
  Global Warming Potential (GWP)
  Ozone Depletion Potential (ODP)
  Human Toxicity Potential (HTP)
  Ecotoxicity Potential (EP)
  Acidification Potential (AP)
  Photochemical Ozone Formation Potential (POFP)
  Eutrophication Potential
  Abiotic Resource Depletion
  Agricultural Land Use

## Slide 15: ReCiPe, Goedkoop et al, 2009
1. Classification
2. Characterisation
Notes: End point structure similar to Eco-indicator 99

## Slide 16: LCA for buildings
Functional Unit:
”1 m2 heated floor area for 50 years” or ”Residence for 12 people for 50 years”
Processes for consideration in inventory:
Once inventory of emissions and resource demands compiled, impact assessment can be performed using generic methods

## Slide 17: Generic Inventory Processes for Buildings – EN Standards 15804 and 15978

## Slide 18: A summary of studies for impact categories GWP and PE

## Slide 19: Simplified LCA procedure
Often called ”life-cycle approach” to avoid confusion with an assessment that follows all rules for LCA according to ISO standard
Assess two processes:
  Product stage
  Operational energy in use stage
One impact category:
  Global Warming Potential

## Slide 20: Interested in LCA?
Jeans !:
http://levistrauss.com/wp-content/uploads/2015/03/Full-LCA-Results-Deck-FINAL.pdf
Building materials and more (EPDs):
http://www.environdec.com/
Courses:
AG2800: LCA course
AG2806: Environmental aspects of the built environment